## Slide 1: Energy Efficiency Potentials in Public Urban Traffic
Institute of Electrical Power Systems
University of Technology Graz
Tongji University

## Slide 2: Theme
Overview Wiener Linien
Importance of energy efficiency
Energy efficiency measures in the metro sector
Energy efficiency measures in the tram sector
Energy efficiency measures in the bus sector
Energy efficiency measures in the infrastructure

## Slide 3: All About Wiener Linien
Operation length
Station
Passenger
2.5 Mio. Passenger/day
640.000 Annual Tickets
Annual Ticket: 365 Euro
5 Metro Line
29 Tram Line
98 Bus Line

## Slide 4: Theme
Overview Wiener Linien
Importance of energy efficiency
Energy efficiency measures in the metro sector
Energy efficiency measures in the tram sector
Energy efficiency measures in the bus sector
Energy efficiency measures in the infrastructure

## Slide 5: Energy Consumption
Energy mix 59% renewable energy
Actual study ecological footprint of Wiener Linien:  appr. 1% of the ecological footprint of Vienna
A view into the energy flow diagram of Vienna  Wiener Linien 5% of the city energy consumption for traffic purposes
Energy consumption
706 GWh per year
Energy costs
61 Mio. Euro per year
Fuel
Heating energy
Electricity

## Slide 6: Energy efficiency
Energy efficiency is part of the corporate strategy and process landscape
Energy efficiency is practiced in all branches of industry
From strategy to planning, new construction to renovation and maintenance
Any further increase in public transport will have a positive effect on the overall traffic energy balance of the city

## Slide 7: Theme
Overview Wiener Linien
Importance of energy efficiency
Energy efficiency measures in the metro sector
Energy efficiency measures in the tram sector
Energy efficiency measures in the bus sector
Energy efficiency measures in the infrastructure

## Slide 8: Vienna Metro System
71 U/U11/U2
51 V
36 T/T1
2,5 Min Fahrintervall Tagesspitze
U1
U3
Simmering
Heiligenstadt
Reumannplatz
Siebenhirten
Hütteldorf
Ottakring
Floridsdorf
U4
U3
U1
U4
U6
U6
Karlsplatz
U2
Leopoldau
Seestadt Aspern
U2
5 lines
79 km
104 stations
158 metro trains
429‚000,000 passengers / year
80 km/h max. speed
70 substations

## Slide 9: Energy Efficiency in Vienna Metro System
Energy optimized automatic operation of metro lines U1-U4
100% vehicles with feedback of traction energy
Energetically optimized duct of lines
Shut-down of trains
LED lighting in all new trains
Research project: Brake Energy
!Measuring values
!development of energy conscious operation
kWh/ train km U1-U4

## Slide 10: Theme
Overview Wiener Linien
Importance of energy efficiency
Energy efficiency measures in the metro sector
Energy efficiency measures in the tram sector
Energy efficiency measures in the bus sector
Energy efficiency measures in the infrastructure

## Slide 11: Vienna Tram System
238 E1/E2
283 ULF A/B/A1/B1
29 lines
177 km
521 trains
  294 Mio. passengers / year
  60 km/h max. speed
63 electrical substations

## Slide 12: Energy Efficiency in Vienna Tram System
84% vehicles with traction energy feedback when braking
Modification of E2 vehicles
ECO Upgrade ULF vehicles
Raising of feedback voltage, shutting down magnetization in idling phases, reduction of Vmax acceleration
Research project: ECO Tram
Testing ULF Energy storage Double layer capacitors
Shutting down of vehicles during standstill
Instruction of drivers
Display of rolling phases percentage in the operator‘s display
!Measuring values
!development of energy conscious operation
kWh/ train km tram

## Slide 13: Eco Tram
Recording the energy profile of a tram type ULF A1
  Measurements in the climate wind tunnel and in passenger service for 12 months
Conversion of a prototype with measures to increase energy efficiency
  Heating / air conditioning systems with heat pump technology
  Frequency variable air conditioning compressors
  Predictive control
  Occupancy-dependent fresh air supply with CO2 sensors
  Window surfaces with heat protection films
Measurements in the climatic wind tunnel and in passenger service for 10 months
  13% of the energy for the HKL system was saved - around 4,200 kWh
  Insights into energy-saving potential in production vehicles and new purchases
funded by

## Slide 14: Gliding % Indication
Drivers‘ support systems
Display of rolling phases percentage in the operator‘s display
Short time (30 sec.)
30-min. mean value
Drivers are encouraged to keep this percentage high

## Slide 15: Theme
Overview Wiener Linien
Importance of energy efficiency
Energy efficiency measures in the metro sector
Energy efficiency measures in the tram sector
Energy efficiency measures in the bus sector
Energy efficiency measures in the infrastructure

## Slide 16: Vienna Bus System
371 LPG
12 Elektro
80 Diesel
98 lines
717 km
469 buses
178 Mio. passengers / year
6 Hybrid

## Slide 17: Energy Efficiency in Vienna Bus System
Modernisation of the car park  EURO 6 Citaro Mercedes
Bus Change over to alternative traction technology:
  2 lines with electric bus
  1 line with hybrid bus
More dedicated bus lanes and traffic light control
Instruction of drivers
Separated from indiviual traffic

## Slide 18: Theme
Overview Wiener Linien
Importance of energy efficiency
Energy efficiency measures in the metro sector
Energy efficiency measures in the tram sector
Energy efficiency measures in the bus sector
Energy efficiency measures in the infrastructure

## Slide 19: Infrastructure
Use of terrestrial heat
5 metro stations
2 train stations
1 office building
1 main workshop
Change of Stations Lighting to LED
Fluorescent tube 36 W at the platform is replaced by LED tube with 20 W.
New Metro stations: Max. use of waste heat
For stations where waste heat from technical rooms is generated, it is used for heating. There is no additional heating system installed..

## Slide 20: Energy Efficiency Potentials in Public Urban Traffic
Institute of Electrical Power Systems
University of Technology Graz
Tongji University